## Slide 1
PE-MMR (SA)
User Guide

## Slide 2
System Requirements
Installation
Program Execution
Troubleshooting

## Slide 3
I. System Requirement
RAM 2GB or More
JDK 1.5 or More (64bit Recommended)
TPP (http://tools.proteomecenter.org/wiki/index.php?title=Software:TPP)
msconvert (Installed as option when TPP is installed)
Thermo Foundation 2.0 (for Q-Exactive)
Xcalibrabur 2.2 (for Q-Exactive)

## Slide 4
II. Installation
Unzip PEMMR_SA_1.1
  log4j (directory)
  pemmr (directory)
  RAPID1.07 (directory)
  PEMMR.cmd (Command Executable File)
  pemmr_sa_param.txt (PEMMR-Parameter File)
  UserGuide.pptx (User Guide)
PEMMR.cmd : Open file in text editor to modify as below
  @echo off
  SET PEMMR_HOME=D:\Programs\PEMMR_SA_Release\1.1 (PEMMR.cmd Change to file existing Directory Address)
  SET CLASSPATH=%PEMMR_HOME%\pemmr\pemmr_sa_1.1.jar;%PEMMR_HOME%\log4j\log4j-1.2.15.jar;%PEMMR_HOME%\log4j;
  set MEM=2048M
  if ""%1""=="""" goto example
  goto exec1
  :example
  echo Example) PEMMR [pemmr_sa_param.txt]
  goto end
  :exec1
  java -Xmx%MEM% pemmr_sa.PEMMRExec %*
  goto end
  :end

## Slide 5
III. Program Execution
Modify pemmr_sa_param.txt as below
Run Command line
Change directory file of PEMMR.cmd (In this case, D:\Programs\PEMMR_SA_Release\1.1)
Run the program typing PEMMR.cmd pemmr_sa_param.txt
PEMMR will create xxxx_PEMMR.mgf which will be used for peptide search
pemmr_sa_param.txt
#################### External Programs ###################
RAPID=D:/Programs/PEMMR_SA_Release/1.1/RAPID1.07/RAPID.exe
MSCONVERT=C:/Inetpub/tpp-bin/msconvert.exe
MZXML2SEARCH=C:/Inetpub/tpp-bin/MzXML2Search.exe
################## UMC Create ##################
RAW_FILE_URL=D:/Programs/PEMMR_SA_Release/1.1/Example/N1_5ug_100cm_300min_1_091112.raw
UMC_ALGORITHM=1
SCAN_COUNT=2
HOLE_COUNT=5
MASS_TOLERANCE=10
MIN_MASS=0
MIN_INTENSITY=0
################## Spectrum Filtering ##################
SCAN_RANGE=5
UMC_LINK_TOLERANCE=10
"Postexperiment Monoisotopic Mass Filtering and Refinement (PE-MMR) of Tandem Mass Spectrometric Data Increases Accuracy of Peptide Identification in LC/MS/MS"
Shin, B.; Jung, H.-J.; Hyung, S.-W.; Kim, H.; Lee, D.; Lee, C.; Yu, M.-H.; Lee, S.-W. Mol. Cell. Proteomics 2008, 7, 1124-1134.

## Slide 6
III. Program Execution (Editing pemmr_sa_param.txt )
pemmr_sa_param.txt
#################### External Programs ###################
RAPID=D:/Programs/PEMMR_SA_Release/1.1/RAPID1.07/RAPID.exe
MSCONVERT=C:/Inetpub/tpp-bin/msconvert.exe
MZXML2SEARCH=C:/Inetpub/tpp-bin/MzXML2Search.exe
################## UMC Create ##################
RAW_FILE_URL=D:/Programs/PEMMR_SA_Release/1.1/Example/N1_5ug_100cm_300min_1_091112.raw
UMC_ALGORITHM=1
SCAN_COUNT=2
HOLE_COUNT=5
MASS_TOLERANCE=10
MIN_MASS=0
MIN_INTENSITY=0
################## Spectrum Filtering ##################
SCAN_RANGE=5
UMC_LINK_TOLERANCE=10
RAPID program is provided with PEMMR and it is located in PEMMR_HOME sub directory
MSCONVERT and MZXML2SEARCH is installed with TPP
RAW_FILE_URL is URL of RAW file under excution
Caution : All directories typed in pemmr_sa_param.txt file should be entered using “/”
e.g.)RAPID=D:\Programs\PEMMR_SA_Release\1.1\RAPID1.07\RAPID.exe (X)
RAPID=D:/Programs/PEMMR_SA_Release/1.1/RAPID1.07/RAPID.exe (O)

## Slide 7
IV. Troubleshooting
Stop running with the message of "java.lang.ClassNotFoundException"
Open PEMMR.cmd file in text editor and make sure the dir of “SET PEMMR HOME location” entered properly.
Q. Execution is interrupted with the message "Exception in thread "main": java.lang.OutOfMemoryError: Java heap space"
Open PEMMR.cmd in text editor and increase MEM to 2048M.
Q. RAPID doesn’t run properly and the file size of resultant files (_isos.csv, _scans.csv) is 0.
A. RAW file has not read properly by the program, Re-Install the Thermo foundation.
If PEMMR program stopped generating result files, need to delete the existing generated files and run the PEMMR once again